## Slide 1: Transport Layer
Data communication and computer networks
Group number - 2
Group Members:
Nihar Singla
Saransh Bhargava
Karan Sharma
Abninav Vaddagiri
Aryan Pratap singh

## Slide 2: Introduction
The transport layer, positioned between the application and network layers, is a key element in network communication. Its primary function is to enable seamless end-to-end communication between applications on different devices. This layer achieves this by breaking down large messages into smaller segments, managing data flow, and ensuring the integrity of transmitted information through error control mechanisms. By regulating the rate of data transmission and overseeing error detection and correction, the transport layer plays a vital role in fostering reliable and efficient communication across computer networks

## Slide 3: Transport Layer Functions
Connection Control
Segmentation and Reassembly
Flow Control (QoS - MUX & Demux)
Regulates the rate of data transfer, ensuring Quality of Service (QoS) by
multiplexing multiple streams and
demultiplexing them at the receiving end.
Congestion Control
Service Point Addressing Identifies and directs data to specific processes running on devices within
a network for precise
communication.
data transmission, ensuring the
integrity of the communicated
information.
Manages the establishment,
maintenance, and termination of
connections for reliable communication.
Prevents network congestion by regulating the flow of data,
optimizing performance, and
avoiding bottlenecks.
Divides large data into
manageable segments for efficient
transmission and reassembles
them at the destination.
Error Control (Error Checking and Recovery
Detects and corrects errors during

## Slide 4: Protocols at the Transport Layer
Transmission Control Protocol
User Datagram Protocol
Connection-oriented protocol
known for its reliability and error recovery mechanisms.
Ensures ordered and accurate
delivery of data, suitable for applications requiring precision.
Connectionless protocol that
prioritizes speed and
efficiency over reliability.
Ideal for real-time
applications like video
streaming and online gaming.
Differences Between TCP and UDP
TCP establishes a connection before data transfer, while UDP does not.
TCP ensures reliable data delivery
and UDP
faster
with acknowledgment retransmission, whereas sacrifices reliability for transmission.
TCP is best suited for applications
where accuracy is critical, while UDP is
preferred for time-sensitive applications.

## Slide 5
TCP Header Format V/S UDP Header Format

## Slide 6: Transport Layer Ports
Within the Transport Layer, port numbers are crucial identifiers for directing incoming data to specific processes or services running on devices engaged in communication. Think of ports as doors or entry points on a device. Each application or service utilizes a unique port number, allowing for organized and efficient data exchange. Well-known ports, like Port 80 for HTTP and Port 443 for HTTPS, are examples of these identifiers. For instance, Port 22 is commonly associated with Secure Shell (SSH), showcasing how port numbers facilitate the proper routing of data to its intended destination process.

## Slide 7: Challenges Faced
Challenges Faced
Congestion: The challenge of network congestion, where increased traffic leads to bottlenecks, affecting the efficient flow of data.
Flow: Flow challenges balance the pace
of data transmission
overwhelming recipients
congestion, ensuring
to prevent or network effective
communication.
Solutions and Technologies Employing sophisticated algorithms like congestion detection + control - warning bit, choke packets, load shedding and congestion avoidance - random early access and traffic shaping.
Implementing flow control strategies like stop and wait and sliding window.

## Slide 8: Flow Control - Stop and Wait
Stop-and-wait is a basic
flow control
technique used in the Transport Layer. In this method, after sending a data frame, the sender waits for an acknowledgment (ACK) from the receiver before sending the next frame. If an ACK isn't received within a specified time, the sender retransmits the frame. This ensures reliable, orderly data transmission.
Advantages: Simplicity.
Each packet is checked and acknowledged before the next packet is sent.

## Slide 9: Flow Control - Sliding Window
Sliding window is another flow control technique used in the Transport layer of the Internet Protocol stack. It manages data transmission by allowing a sender to transmit multiple packets without waiting for individual acknowledgments. The receiver specifies a window size, dictating how many packets it can accept at once. TCP acknowledges receipt of data to the sender, and keep advertising new receive windows to the sending system. If the receive buffer is full, the receiving system advertises a receive window size of zero, and the sending system must wait to send more data.

## Slide 10: Conclusion
In conclusion, the Transport Layer serves as the backbone in data communication and computer networks, arranging a reliable and secure information exchange. We've explored its key functions, protocols like TCP and UDP, and witnessed the impact of advancements such as QUIC on communication speed. As we address challenges through congestion control, latency reduction, and robust security, the future holds exciting prospects. Anticipated trends include further optimization for high-demand applications, the integration of artificial intelligence in congestion management, and continuous innovations in security protocols to adapt to evolving cyber threats. The Transport Layer's evolution promises a future of even more agile, responsive, and secure communication networks.

## Slide 11: Thank You F o r Y o u r A t t e n t i o n